| Method Statement for: | Installation of the Sole Plates |
| --- | --- |
| Client: William Langton, C.W. Langton Developments | Site: Cockcroft House, Cardigan Road, Hyde Park, Leeds LS6 3NF |
| Appointed site supervisors & contact numbers: |
| Method of Works: |
| Prior to Works: Inspect equipment for signs of damage prior to use Ensure suitable PPE is supplied & worn as required Ensure relevant tools & equipment are available Position site security fencing around the work area |
| During Works: The base for the building will be measured ensuring the dimensions are correct The location of the sole plates will be measured and marked out Levels will be taken across the foundation checking for high and low spots The sole plate timbers will be selected and inspected to ensure that they are free from damage, warp, twist and bow Timbers will be laid at the highest point along the previously marked line The first sole plate will be aligned and secure to the floor with suitable fixings further sole plate timbers will be laid and aligned with packers placed under them to ensure that they are level throughout the building The dimension’s will continue to be checked against the design detail Once all the sole plates are in place they will be re measured and checked for dimension, ensure that they are square and level |
| Completion of Works: Ensure that any waste materials are swept up and disposed off All tools are stored away in a secure area or removed from site at the end of the shift The site is secured at the end of each shift Ensure that access controls and routes are in place and signed |
| Site Specific Details |
| Deliveries of panels via articulated vehicles shall be driven into the site then reversed back to the turning area with an appointed employee over seeing all reversing activities Cease lifting operations should an unauthorised person enter the work area Use the clients / principal contractors welfare facilities with respect |

| PPE Requirements: |
| --- |
| Safety helmets Safety footwear High visibility vests Gloves Goggles Hearing protection as required |
| Equipment Requirements: |
| Dumpy Level Drill Screws and fixings Hand tools as required |
| Date: 14th December 2015 | Review Date: A required during works |
| Sign: | Print: Ian Clay – SISP@Clays Mark Holmes – M H Safety Ltd |
| Employees Sign: | Employees Print: |